## Slide 1
Utilizing Engineered Permeable Reactive Caps To Minimize Re-Suspension Of COC – Post Dredge
WEDA Midwest Chapter – Green Bay
April 27, 2012
Allen Bullock
CETCO Remediation Technologies
PRESENTED BY:
Notes: 1

## Slide 2: Challenges Mitigating Contaminated Sediments
Dynamic conditions
Multiple transport mechanisms
Multiple types of contaminants
NAPL becomes very visible in surface waters
Potential re-distribution/re-suspension
Courtesy USEPA, CLU-IN

## Slide 3
2005 US EPA Guidance on Contaminated Sediment Remediation
Adaptive Management
Risk Mitigation Approach
Notes: Published December 2005

## Slide 4: Traditional Cap Function/Design Objective
  Reduce risk by
  Stabilizing sediments
  Physically isolating sediment contaminants
  Maintaining permeability with groundwater and gas ebullition transport
  Reducing contaminant flux to benthos and water column
  Reactive Capping to enhance chemical isolation
Source: D. Reible, Sediment Remediation – How do you select design options, Portland, OR, 2007
Notes: 4

## Slide 5
Reactive Layer
Conceptual Cap Designs – Permeable Reactive Cap
Thin Sand Cap
Contaminated
Sediment
Reactive Cap
Bioturbation
Erosion Control
Thick Sand Cap 2’- 3’
Bioturbation
Erosion Control
Contaminated Sediment
Traditional ISC

## Slide 6: Benefits of Permeable Reactive Caps
  Physical AND chemical isolation of contaminants of concern
  Quickly reduces exposure risk
  Allows for continued preferred movement of ground water sources
  Allows for gas ebullition
  Minimizes cap thickness
  Clean substrate for re colonization of benthic organisms
Notes: 6

## Slide 7: Potential Reactive Cap Media
Clays for permeability control
Activated Carbon or other carbon sequestration agent
Organoclays for NAPL control
  Demonstrated (e.g. McCormick and Baxter)
  Significant swelling and permeability reduction with NAPL
  Design balancing capacity with permeability reduction
Phosphate additives for metals
  Rock phosphate (e.g. apatite) demonstrated
  Phytic acid salts, injectable into sediments
Siderite (FeCO3) for pH control
Zero valent iron
Oxygen or hydrogen release compounds/technologies
Biopolymers
  Can sorb metals and organics
  May provide erosion control and suitable surficial substrate
  May provide carbon source to enhance microbial activity
Demonstrated
Speculative
Source: D. Reible, Sediment Remediation – How do you select design options, Portland, OR, 2007
Notes: 7

## Slide 8
Source: www.epa.gov/glnpo/aoc
Project Overview
Project Started in 2009
GLLA Funding: 65%
Design Engineer: Tetra Tech EM
Multiple year project – 2 phases:
  Reach 3 (Completed 2009)
  Reaches 4-5 (Completed 2010)
  Reaches 1-2 & Roxana Marsh (To Be Completed 2012)
NAPL, PCB, PAH, & Metals
Sediment clean up, capping, habitat restoration
GREAT LAKES NATIONAL PROGRAM OFFICE
Grand Calumet River West Branch

## Slide 9
Completed over 2 seasons: 2009 & 2010
1 Mile Stretch of Impacted Area
PAH, Heavy Metals, NAPL, PCB
Source: www.epa.gov/glnpo/aoc
Phase 1: Reach 3 & Reaches 4-5
Removal of 150K yd3 Sediment
App. 650K ft2 Reactive Cap
Reactive Core Mat - GAC
R-3
R-4,5

## Slide 10
Very soft sediment
Debris
Bank Stability issues
Site Challenges
Dewatering Solids for disposal
QC/QA systems to verify cap
Populated area

## Slide 11
Project Highlights
Sevenson Environmental
Mechanical Dredge
Dewatering Pad
Reactive Core Mat (RCM) – GAC filler
Minimum 240 year design life
2 foot armoring layer
Cap placement in “Dry”
Geogrid utilized to improve bearing capacity
RCM allowed for termination at sheet piling in R4
Notes: Draw out project on board…how they cut off river, diverted flow, etc.

## Slide 12
Project Summary
Project completed on schedule for both phases
Lessons learned from R3 benefitted efforts in R4-5
Natural habitat starting to recover

## Slide 13: CETCO Reactive Core Mat® (RCM)
Features
RCM consists of a layer hydrophobic media encapsulated between two geotextiles
Needle-punched to provide internal reinforcement
The internal reinforcement minimizes media from shifting
Added geotechnical properties for soft sediment concern
Can be deployed in dry or sub aqueous conditions
¼”

## Slide 14
Reaches 1-2 & Roxana Marsh work under way
GLLA funding 65% of projected costs ($50M)
JF Brennan primary GC
Removal of 222K yd3 Sediment: 122K from River
  and 110K from Marsh
Hydraulic Dredge and Mechanical Excavation
Bulk reactive cap/Armoring Layer in River
Organoclay PM199®/Sand
420 Year design life
Thin lift placement with BCSTM
Source: www.epa.gov/glnpo/aoc

## Slide 15
Summary
Reactive Caps can greatly reduce the long term risk of contaminant re-suspension
Can be implemented quickly, reducing exposure
Offer physical and chemical isolation thus reducing the cap profile
Several types of reactive media successfully demonstrated
Media can be deployed in bulk and within geocomposite mats (RCM)
Thin lift placement (< 6”) should be utilized for bulk deployment
RCM performs multiple cap functions:
  Promote uniform consolidation
  Prevents mixing of cap material with underlying sediment
  Added bearing capacity for soft sediment concerns
  High internal shear strength – added slope stability

## Slide 16: Thank You for Joining Us!
A PDF copy of the presentation
can be provided to you upon request
Presenters
Allen Bullock
Technical Sales Manager
CETCO Remediation Technologies
allen.bullock@cetco.com